## Slide 1: Polarized Backscattering with high Resolution
E. Babcock, M. Zamponi, S. Mattauch
@

## Slide 2: History / back-story for polarized QENS
Wide angle inelastic PA, SM based, DNS and D7
  Direct geometry and compact, resolution limited to about 100 meV
PASTIS, 3He based (but uniaxial) also on direct geometry gives a taste of polarized QENS
  LET @ ISIS experiments on D2O (published) max resolution 22 meV
  NEAT @ HZB with JCNS exp. on H2O (in process) max resolution 50 meV, but lower Qmin
These experiments raise interest for QENS measurements with PA
  e.g SHERPA workshop at ISIS, inverted geometry for pulsed sources, proposed resolutions >10 meV
Many projects and proposals for PA with >10 meV resolution
Power of continuous source backscattering is resolution of 1 meV or better
MORIS project may enable us to work on an instrument with UNIQUE properties utilizing the strengths of the FRM2 source

## Slide 3: Usual Chart of applications (from ESS webpage)

## Slide 4: Scientific case Polarized Backscattering with high Resolution
Measurement of incoherent QENS in presence of coherent
Coherent scattering is often concentrated in certain Q ranges (Bragg peak, amorphous halo, SANS), making these inaccessible
Klenk et al., Solid State Ionics 312, 1 (2017)
Li- self-diffusion in Li garnet oxide @ BASIS
700K

## Slide 5: Scientific case PBR cont.
Measurement of coherent QENS in presence of incoherent
Incoherent scattering often dominant despite high degree of deuteration
- Typical H/C ratio in an organic material is 2/1. With 95% deuteration this gives still 42% incoherent scattering
Heavy water @ LET
Arbe et al., Physical Review Research 2, 022015 (2020)

## Slide 6: Scientific case PBR cont.
Measurement of coherent and incoherent QENS on same sample
Could be done on one sample if: - coherent and incoherent scattering can be separated - nanosecond timescale can be reached (equivalent µeV resolution)
Confined ionic liquid-water mixtures @ WASP
Frielinghaus et al., Front. Phys. 10, 872616 (2022)
incoherent coherent scattering dominating
polarized intensity

## Slide 7: Scientific case PBR cont.
PA-QENS a current scientific ‘hot topic’ however: Current proposals do not consider resolution <10µeV
=>Therefore complementary science case for sub-µeV PA

## Slide 8: The laws of applying polarization
Do no harm to the unpolarized instrument
Only apply PA when there is a strong theroretical or experimental justification
Steady polarization, polarization as an instrument component, is best but don‘t forget law 1 (or 2)

## Slide 9: Where can Polarization components go?
For traditional backscattering the beam is focused back trough the sample, angular divergence for SM solutions is the usual
  Q=W/2d
3He solutions are „divergence independent“, However have limitations of needing to be actively polarized/or exchanged regularly, need to be close to the SE
Any solution will need a magnetic guide field over the entire analyzer tank
Polarization Analyzer

## Slide 10: Guide field
Simply add a large Helmholtz coil
At 2.5m=R need 2800A/turns for a coil pair for 10gauss
200 turns at 14 A with 3mm wire
  3.2 kW, ~45 euro/day
  about a 5x5cm coil,
  590 kg copper
Would also provide the magnetic enviroment for 3He
Field would be constant: no time changing influence on other instruments

## Slide 11: SPHERES

## Slide 12: 3He analyzer option
Active polarization
  In-situ ----steady
  Ex-situ---- decaying
Tn=30% at Pn=94% (in-situ)
In principle large angular coverage and any sample size
Qmin>0.5 Å-1 from cell geometry and position
Fundamental limit from geometry
Small angle detectors are out of backscatering geometry, could be covered with a second cell(s)
Radial collimator starts at r=8cm, small angle detectors also very close
Ex-situ polarization would require separation of the Ar flight path
In-situ polarization requires thermal management, but possible in Ar or vacuum
ID=8cm
OD=16cm
Pastis1 cell
6 bar cm
Beam
Second cell

## Slide 13: Traditional reflection SM analyzer option
Make extrapolations based on the “new” D7 analyzers:
J.R. Stewart et al., J. Appl. Cryst. 42, 69 (2009).
lmin=3.1Å, d=1250mm, W=30mm
6.27Å and W=30mm at 625mm+250mm
to detectors, which are 250mm high
20mm sample d becomes 416.6mm, detectors at 666.6mm
current SPHERES has about 53°vertical
SM at 875mm would have 16°
at 666.6mm about 21°
double the height, i.e 2x250mm then >42°vertical
Simply NO space in the current configuration

## Slide 14: What about after the sample, i.e. between sample and Si analysers?
Neutrons pass the polarization analyzer twice
Diffraction background of 3He cell requires a collimator?
SM transmission analyser + integrated collimator
inelastic effects on neutron energy at 𝞵eV level?
Collimation (if needed) could be problematic for SANS detectors

## Slide 15: In-situ polarization?
Ar flight path on SPHERES
  Cell exchange would be difficult
  For in-situ polarization 100‘s of watts are provided by the optical pumping lasers
  Laser power and heat loss to radiation are comparable at SEOP conditions (180 ˚C)
Will a collimator be required because of the cell?

## Slide 16: Does GE180 affect (energy) resolution
Spectrum measurements on TOFTOF (G. Simeoni)

## Slide 17: „WAPA“ Transmission SM analyser
In principle double pass should also be possible
Similar divergence consideration as reflection analyzer
  Array at d=416 mm for a 20 mm sample, >500mm high
Again, Collimation could be problematic for SANS detectors
=> Here it is intrinsic
P. Böni et al., Nuclear Inst. and Methods in Physics Research A 966, 163858 (2020)

## Slide 18: Small angle analyzers and detectors Q<0.5Å
J. Wuttke, M. Zamponi, Rev. Sci. Instrum. 84, 115108 (2013)

## Slide 19: Expected performance SM or 3He
Either SM or 3He could provide Tn>20% and Pn>95%
Given 2/3 spin flip for incoherent scattering one would expect Iincoh≈15% of the unpolarized instrument
Coherent scattering Icoh≈20% (minus 1/2*Iincoh)
Flipping ratios F>25 assuming incident polarization >97%
Roughly 5x less counts but 25x higher S/N (contrast) before PA corrections
=> Would PA cause a significant change in measurement time for „standard“ measurments?
With PA the „extra“ measurement separates coherent and incoherent contributions

## Slide 20: Common challenges
Guide field
Incident beam polarization and flipper
Sample to detector distance
To be made removable
Both capable of “full“ analyzer coverage with work
SM would limit sample width to maintain polarization performance
Collimation intrinsic for transmission SM
In-situ 3He polarization a must / active system
Key differences

## Slide 21: Summary
Good scientific motivation for an instrument with UNIQUE capability
Major components technically feasible but a challenge to fit into existing instrument
Detailed study simulation + testing required to compare SM and 3He

## Slide 22: acknowledgements
Reiner Zorn
Jörg Voigt
Olaf Holderer
Klaus Lieutenant
Margarita Russina (HZB)

## Slide 23
Thank you
for your
attention!